## Slide 2
Actuators
(12 DC Motors)
Optocoupler + Relay
(3 rows of 4 motors)
Sensors
(1 End stroke per motor)
Datalogger
Emergency Button
Optocoupler
(1 each line)
Computer
Current Generator
Optocoupler
(1 each line)
Arduino
Mega
Interrupts

## Slide 3: BOM
Item | QTY | Datasheet
Arduino Mega | 1 | 
Motors | 12 | 
End Stroke | 24 | 
DPDT Relays | 3 | 
Optocoupler | 7 | 
Emergency Button | 1 | 

## Slide 4: Inputs & Outputs
Component | Arduino Input | Arduino Output
Actuator |  | Can_move Move_forward Move_backward
End stroke | Is_close | -
Datalogger | Is_allarm | -
Generator | Test_end Test_in_progess Test_stopped | Start_cycle Stop_cycle Enable
Emergency switch | Is_pressed | -
Door switch | Door_closed | 
User interface | Start_test Stop_test End_test | -
*Optional

## Slide 5: User interface
Test type
Mating test
High load
Annex LL
Test cycles
248
Ton[h]
2
Toff[h]
1
Test duration: 42 days
Start time : 30/11/2021 15:06
End time : 11/01/2022 17:06
Start test
Cycle duration: 3h
Stop test
Test status: In progress
Current cycle : 12/248
Cycle Phase : Current On
Phase timer: 0:27:15